# To remember

energy transferred = power ( time

efficiency =

current =

This is a special care cot for a new-born baby. It monitors the temperature and includes a heater which is switched on and off automatically.

This is the rating plate.

# To answer

To build a circuit to monitor temperature, a component is needed that changes resistance as it gets hotter or colder. 
(You can read about this in Section D of your Textbook.)

What is this component called?

Draw a circuit symbol for it.

For this component, does the resistance increase as the temperature increases, or does it decrease?

Look at the rating plate. (You can read about this in Section G of your Textbook.)

If the cot uses full power all the time:

How much energy will it use in 1 second? (Give your answer in joules.)

How much energy will it use in 24 hours? (Give your answer in kWh.)

The actual energy used in one 24-hour period is 4kWh. 
Why is this less than your answer to question 5?

A unit (1 kWh) of electricity costs 10p. How much did it cost to run the cot on this day?

In one minute the cot gives out 18 000 J of useful energy (mostly heat).

Work out the electrical energy used (in joules) in one minute.

Work out the efficiency of the cot.

If the mains voltage is 230 V, use the equation I =  to work out the maximum current the cot takes.

An electrician has a choice of a 1 A, 3 A, 5 A, or 13 A fuse. Which one should she fit?

Explain your choice for question 10.

Here are four phrases that describe how a fuse works, but they have been muddled up. Put them in the correct order:

  - This causes a break in the circuit so the current stops flowing

The fuse contains a thin piece of wire

At a certain current it will melt

The higher the current the hotter this piece of wire gets until

# Text boxes

Cover B  sheet 1

Cover B  sheet 2